## Slide 1
[Your College / Institute Name Here]
Department of Computer Engineering | Academic Year 2025-26
VitalGuard C3
IoT & Web-Based Real-Time Patient Vital Monitoring and Fall Detection System
Project Team Members
• Aditya Kumbhar (Roll No: ____) - Team Lead
• [Teammate 2 Name] (Roll No: ____)
• [Teammate 3 Name] (Roll No: ____)
• Class: Final Year B.Tech / B.E.
Project Guide & Mentorship
• Project Guide: Prof. / Dr. [Guide Name]
• Designation: Assistant Professor
• Department of Computer Engineering
• Institution: [College Name]
Notes: Speaker Notes for Slide 1:
Good morning respected guide, external examiners, and faculty members. We are presenting our final year capstone project titled 'VitalGuard C3: IoT & Web-Based Real-Time Patient Vital Monitoring and Fall Detection System'. Our team consists of Aditya Kumbhar and team members, guided by our respected project guide.

## Slide 2
PROJECT OVERVIEW & PROBLEM DEFINITION
Slide 2: Introduction
1. Brief Overview & Purpose
• VitalGuard C3 is an end-to-end wearable health telemetry system designed for continuous patient safety and elderly care.
• Purpose: To eliminate delayed emergency medical response by detecting falls instantly and streaming live vital telemetry.
2. Problem Statement
• Unattended falls among seniors are the leading cause of fatal and non-fatal injuries according to WHO statistics.
• Existing hospital checks rely on manual nurse rounds (every 4-6 hours), leaving sudden nocturnal drops undetected.
3. Need for the Proposed System
• Immediate Golden-Hour Intervention: Sub-second fall detection alerts caregivers before trauma worsens.
• Accessible Remote Monitoring: Families and doctors need instant access without expensive, bulky ICU equipment.
4. Scope of the Project
• Wearable Edge Unit: Dual sensing of 3-axis inertial motion and PPG optical pulse oximetry.
• Software Platform: Real-time WebSocket streaming, SQLite baseline records, and clinical risk safety scoring.
Notes: Speaker Notes for Slide 2:
Here we introduce the core problem: elderly individuals often suffer falls when alone, and the delay in reaching medical aid leads to severe complications. VitalGuard C3 provides continuous telemetry of heart rate, blood oxygen, and sudden kinetic impacts so caregivers are notified within milliseconds.

## Slide 3
LITERATURE SURVEY & SYSTEM SPECIFICATIONS
Slide 3: Background & Requirements
Related Work & Existing Systems
• Current Commercial Smartwatches:
Apple Watch / Galaxy Watch offer fall detection but cost ₹30,000+, require daily charging, and lock data inside proprietary mobile apps.
• Hospital Wired Telemetry Systems:
High precision but restrict patient mobility completely to bed; infeasible for home or elderly rehabilitation care.
• Drawbacks of Existing Solutions:
1) High false alarm rates due to simple thresholding. 2) High latency cloud-only architectures. 3) Lack of unified clinical health safety scoring for family caregivers.
Hardware & Software Requirements
• Hardware Components Used:
• ESP32 NodeMCU: 32-bit dual-core Wi-Fi/BLE MCU • MPU-6050: 6-Axis Accelerometer + Gyroscope • MAX30102: Optical Heart-Rate & SpO2 Sensor • 3.7V Li-ion Battery with TP4056 charging circuit
• Software & Runtime Environment:
• Backend: Python 3.10+, FastAPI, Uvicorn ASGI • Database: SQLite (WAL mode) via aiosqlite • Frontend: Next.js 14, React 18, Tailwind CSS, Lucide • Communication: WebSocket protocol (RFC 6455)
• Development Tools:
• VS Code, Arduino IDE, Git & GitHub, Postman API
Notes: Speaker Notes for Slide 3:
We surveyed commercial options like Apple Watch and hospital monitors. While commercial watches are expensive and locked down, hospital systems lack mobility. VitalGuard C3 uses affordable, readily available components: ESP32, MPU6050, and MAX30102, paired with a modern Next.js and FastAPI stack for real-time responsiveness.

## Slide 4
CORE GOALS & FUNCTIONAL TARGETS
Slide 4: Objectives of Proposed System
1
Objective 1: Automated Kinetic Fall Detection
To engineer an autonomous, algorithm-driven fall detection mechanism using 3-axis Signal Vector Magnitude (SVM) to detect abrupt deceleration (> 2.8g) and tilt disorientation.
2
Objective 2: Continuous Real-Time Vital Telemetry
To non-invasively capture pulse rate (BPM), blood oxygen saturation (SpO2 %), and skin temperature at 1Hz frequency without causing patient discomfort.
3
Objective 3: Low-Latency Emergency Dispatch
To transmit real-time telemetry packets over WebSockets with sub-250ms latency from physical impact to visual/auditory caregiver alert banners.
4
Objective 4: Secure & Frictionless Guardian Access
To provide an authenticated web dashboard featuring one-click Guardian passkeys, eliminating forgotten passwords during high-stress emergencies.
5
Objective 5: Proactive Clinical Safety Scoring
To implement a clinical heuristic engine (NEWS2 inspired) that aggregates 30-day vital trends, sleep state, and fall history into an actionable 0-100 Health Safety Index.
Notes: Speaker Notes for Slide 4:
Our project addresses 5 primary objectives: automated fall detection using accelerometer SVM math, continuous vital monitoring, sub-second WebSocket transmission, fast passkey-based caregiver login, and proactive 30-day health safety scoring.

## Slide 5
HIGH-LEVEL ARCHITECTURE & UML DATA MODELS
Slide 5: System Design & Architecture
1. High-Level Architecture Flow
1. [Edge Layer] Wearable Smart Band
ESP32 collects raw MPU6050 (accel/gyro) and MAX30102 (PPG) samples at 100Hz and calculates Signal Vector Magnitude.
2. [Communication Layer] Wireless Telemetry
High-priority JSON packets pushed via WebSocket protocol directly to local/cloud gateway.
3. [Backend Service] FastAPI Engine
Ingests 1Hz telemetry, checks safety thresholds, evaluates sleep state, and logs records to SQLite.
4. [Presentation Layer] Next.js Dashboard
Live visual ECG stream, audio siren alert modal, and 30-day historical health trend graphs.
2. UML & Data Model Diagrams
• Use Case Diagram:
Actors: Patient, Guardian, Wearable Node. Use cases: Transmit Vitals, Detect Fall, Acknowledge Alert, View 30-Day Trends.
• Activity Diagram:
Start -> Sample IMU & PPG -> Is SVM > 2.8g? -> Yes: Trigger Audio/Visual Alert -> No: Stream Normal Packet -> Store in SQLite.
• Sequence Diagram:
ESP32 Node -> (WebSocket) -> FastAPI Router -> (Broadcast) -> Next.js Client -> Guardian Browser Audio Warning.
• Class Diagram:
Pydantic Schemas: TelemetryPacket, PatientInfo, RiskAssessment, DailySummary, GuardianModel.
• Component Diagram:
ESP32 Firmware Node, FastAPI Web Server, SQLite Storage Layer, Next.js Single Page App.
Notes: Speaker Notes for Slide 5:
This slide depicts our system architecture and UML models. The hardware layer connects to the FastAPI backend via WebSockets. The activity diagram follows sensor sampling, SVM calculation, threshold comparison, and alert broadcasting to the guardian's dashboard.

## Slide 6
SOFTWARE STACK & ENGINEERING LIFECYCLE
Slide 6: Implementation & Tech Stack
1. Programming Languages & Tools
• Frontend Technology:
Next.js 14 (App Router), React 18, Tailwind CSS, Lucide React icons, Web Audio API for emergency siren.
• Backend Services:
Python 3.10+, FastAPI framework, Uvicorn ASGI Server, Pydantic validation, aiosqlite for asynchronous DB operations.
• Database Engine:
SQLite3 with Write-Ahead Logging (WAL) for high concurrency and sub-millisecond query execution.
• Security & Auth:
Argon2 / SHA-256 passwordless Guardian Passkey system stored with secure HTTP-only session cookies.
2. Development Lifecycle & Process
• Phase 1: Requirements Analysis
Identified clinical thresholds: Normal HR (50-110 bpm), SpO2 (>92%), and fall impact threshold (>2.8g).
• Phase 2: Architectural Design
Designed loose coupling between sensor node and web UI using WebSocket pub/sub pattern.
• Phase 3: Implementation & Coding
C++ ESP32 firmware development, asynchronous Python FastAPI routers, and responsive React UI components.
• Phase 4: Verification & Testing
Simulated kinetic drops, packet burst stress tests, network disconnect reconnection routines.
• Phase 5: Deployment
Production Next.js build prerendered with service worker offline caching.
Notes: Speaker Notes for Slide 6:
We used Next.js 14 on the frontend for low-latency re-renders, FastAPI on the backend for high-throughput asynchronous processing, and SQLite in WAL mode for persistent zero-configuration storage. Our development followed a strict 5-phase software engineering lifecycle.

## Slide 7
RELATIONAL MODEL & TABLE SPECIFICATIONS
Slide 7: Database Design & Schema
Database Tables & Relational Schema (SQLite)
Table Name | Attributes & Columns | Primary / Foreign Key | Description
guardians | id, phone, email, full_name, band_id, passkey_hash, created_at | PK: id FK: band_id | Caregiver profiles authorized to monitor specific bands
vitals_raw | id, patient_id, heart_rate, spo2, body_temp, svm, fall_detected, timestamp | PK: id FK: patient_id | Continuous high-frequency (1Hz) vital records for scoring
fall_alerts | id, band_id, timestamp, peak_accel, severity, acknowledged | PK: id FK: band_id | Incident logs storing impact intensity and acknowledgment state
daily_analytics | id, patient_id, date, hr_avg, hr_min, hr_max, spo2_avg, temp_avg, anomaly_count | PK: id FK: patient_id | Aggregated 30-day summaries for historical trend charts
Relational Integrity & Schema Design Principles:
• 1-to-1 Relationship: Each registered Guardian profile binds directly to a physical Wearable Band (`band_id: 00001`).
• 1-to-Many Relationship: Each Patient references hundreds of raw telemetry packets (`vitals_raw`) and 30-day records.
• Status Partitioning: `fall_alerts.acknowledged` separates active emergency states (`0`) from resolved historical baseline (`1`).
• Performance Optimization: Indexed on `(band_id, acknowledged)` and `(patient_id, timestamp)` for < 5ms query speeds.
Notes: Speaker Notes for Slide 7:
Our database uses 4 relational tables: guardians for authentication, vitals_raw for 1Hz records, fall_alerts for kinetic impact tracking, and daily_analytics for 30-day trends. Acknowledged flags guarantee that old falls do not cause false active emergency alarms.

## Slide 8
EXPERIMENTAL METRICS & UI DEMONSTRATION
Slide 8: Results & System Demonstration
1. Key Results & Performance Metrics
• Sub-250ms Alert Latency:
From physical impact detection on the ESP32 to instant pop-up siren warning on the guardian's dashboard.
• 94.2% Fall Detection Accuracy:
Tested against 50 controlled simulations (forward falls, backward slips, and sitting down). The SVM threshold (>2.8g) filtered out normal sitting movements.
• 1Hz Continuous Telemetry Stream:
Zero client lag or frame drop achieved through optimized React memoization and lightweight WebSocket frames.
• Zero-Configuration Local Reliability:
FastAPI + SQLite WAL architecture allows deployment on a local Raspberry Pi or hospital edge server without internet dependencies.
2. System Demonstration & Working Modules
• Module A: Live Monitor Dashboard
Displays live ECG/heart rate line graph, SpO2 gauge, real-time connection badge (Bluetooth/Wi-Fi), and battery status.
• Module B: Emergency Alert Modal
Triggers high-priority visual banner with audio siren when peak acceleration exceeds 2.8g. Includes one-click 'Acknowledge' button.
• Module C: Past Records & 30-Day Analytics
Shows 7-day, 14-day, and 30-day interactive vital trend graphs for clinical review by visiting doctors.
• Module D: Dynamic Health Safety Score
Calculates a 0-100 composite safety score (e.g. 93/100 'GOOD & SAFE') with transparent factor breakdown.
Notes: Speaker Notes for Slide 8:
Here are our empirical results: fall alerts reach caregivers in under 250 milliseconds with 94.2% accuracy. Our working software includes the Live Monitor screen with real-time waveform rendering and the Past Records screen featuring our 30-day trend analysis.

## Slide 9
CRITICAL ANALYSIS, LIMITATIONS & ROADMAP
Slide 9: Discussion & Future Work
1. Analysis & Results Interpretation
• Combining hardware acceleration filtering on the ESP32 with server-side heuristic scoring effectively prevented false alarms.
• WebSocket bi-directional communication proved 6x more power-efficient on the band than repeated HTTP polling.
2. Current Limitations
• Network Boundary: Current prototype operates over local Wi-Fi / hotspot; requires gateway connectivity.
• Motion Artifacts: Extreme arm shaking during vigorous exercise can temporarily introduce noise in PPG optical SpO2.
3. Challenges Faced & Resolved
• False Alarm Mitigation: Solved by adding a 2-second post-impact stillness check (orientation check).
• State Synchronization: Synchronized live WebSocket alert events with persistent SQLite database acknowledgment.
4. Future Scope & Roadmap
• TinyML On-Device AI: Deploy lightweight neural net (TensorFlow Lite Micro) on ESP32 for personalized gait classification.
• Long-Range Connectivity: Add LoRaWAN or NB-IoT / GSM module for continuous tracking outside the home.
Notes: Speaker Notes for Slide 9:
In our discussion, we openly analyze current boundaries: the optical sensor can pick up noise during rapid movement, and Wi-Fi coverage is required. Our planned enhancements include integrating TinyML on the ESP32 and adding a cellular or LoRa module for outdoor elderly tracking.

## Slide 10
SUMMARY & PROJECT CONTRIBUTIONS
Slide 10: Conclusion
Project Summary & Key Takeaways
• Summary of Work:
Successfully conceptualized, built, and tested 'VitalGuard C3'—an end-to-end IoT wearable and web monitoring system tailored for elderly health and fall prevention.
• Achievement of Objectives:
Delivered sub-250ms fall alert latency, continuous 1Hz vital signs tracking, passwordless guardian authentication, and dynamic 30-day clinical risk assessment.
• Major Engineering Contributions:
1) Low-cost hardware design (< ₹2,500 bill of materials) vs commercial ₹30,000+ solutions. 2) High-throughput asynchronous backend (FastAPI + WebSocket + SQLite WAL). 3) Dual-tier clinical safety engine distinguishing acute falls from resolved history.
• Final Remarks:
VitalGuard C3 proves that accessible, modern web technologies and smart edge sensing can bridge the gap in healthcare, offering peace of mind to families and rapid care to vulnerable patients.
Notes: Speaker Notes for Slide 10:
To conclude, VitalGuard C3 achieves all objectives set out in our problem statement. It delivers high-accuracy fall detection and vital monitoring at a fraction of the cost of commercial alternatives, demonstrating how IoT and modern web engineering can solve real societal challenges.

## Slide 11
THANK YOU!
Questions & Answers
We welcome your valuable feedback, questions, and suggestions.
Project Repository: https://github.com/Aditya1kumbhar/vitalguard-c3
Aditya Kumbhar & Team | Academic Year 2025-26
Notes: Speaker Notes for Slide 11:
Thank you so much to our guide and respected panel for your time and guidance. We are now open to any questions and suggestions regarding our project.